## Slide 1: IEC 61400-11-2 Receptor Sound Measurements
Mark Bastasch, P.E. (OR), INCE Bd. Cert. Principal Acoustical Engineer

## Slide 2: IEC 61400-11-2: Measurement of wind turbine noise characteristics in receptor position
IEC 61400-11 establishes uniform methods to determine apparent sound power levels, measured close to the turbine
IEC 61400-11-2 is intended to address the measurements of sound pressure levels and noise characteristics at further distances, typical of residences or other compliance points
  Measurements at further distances, where the sound attributable to the turbine is less, may be complicated by background levels (poor signal to noise ratio)
Intent is to be a Technical Specification rather than an International Standard
  Releasing as an International Standard considered premature

## Slide 3: IEC 61400-11-2: Measurement of wind turbine noise characteristics in receptor position
Regulatory requirements at receptors not uniform throughout the world
  Denmark (Scandinavia) evaluates sound outdoors and indoors via modeling
  UK focuses evaluation of trends in sound levels (and amplitude modulation)
  Tonality assessed a variety of ways
IEC 61400-11-2 is intended to provide guidance/best practices to address a variety of regulatory requirements
  Describe available and reliable methods
  Develop “toolbox” from which an expert can pick the best approach for the required assessment
  Assist those countries that don’t have strong regulatory history

## Slide 4: Test Planning
The purpose is to give guidance for the measurements to secure robust valid results.
Setting up a test plan is the key to this as it should address the measurement conditions and the environment in detail before the measurements are initiated:
  Purpose of the measurements: Sound presure level, AM, Tonality, Low Frequency noise
  Quality of the site: Ambient noise, Representative conditions, ….
  Receptor locations and microphone setup.
  Instrumentation requirements: Overall levels, 1/3-octave band, FFT, …
  Wind speed determination methods
  Other atmospheric conditions that impact noise generation and propagation

## Slide 5: Structure of the Document
Main chapters are:
  Instrumentation. Requirements for different types of instruments including periodic calibration
  Test Planning
  Sound Pressure Level determination. Several methods.
  Tonality. Will be based on ISOPAS 20065, which is an FFT based method.
  Amplitude Modulation Will be based on UK methods
  Impulsivity. Will be based on a Nordtest standard which will also be an ISO method
  Reporting

## Slide 6: Structure of the Document
Annexes (informative) on
  Rating Level (i.e., penalties)
  Infrasound
  Low Frequency Noise evaluation
  Examples for guidance
  Tonality
  Data Exclusion Tools
  AM Adaptions
  Secondary wind screens / Facade mounted microphone / Proxy location
  Sound Emergence (i.e., increase over existing)
  Meteorological Effects

## Slide 7: IEC 61400-11-2 Team
Mr. Bo Søndergaard of Sweco Danmark A / S, leader of the MT11 maintenance team, is leading this effort.
  Ms Sylvia Broneske of RWE UK is serving as secretary
  United States membership includes Arlinda Huskey/NREL and Mark Bastasch/Jacobs joined in December 2019.
  Membership has strong European focus
  Canada is an active participant
  Participants from India, China, Japan
In-person meeting in fall 2019 and hybrid meeting early March 2020
Biweekly weekly online meetings April-December 2020, weekly January to (April?) 2021

## Slide 8: IEC 61400-11-2 and USA
Measurement approaches in the USA differs somewhat from EU
  Measurement of centerline trends used in the UK, whereas USA assessments tend to focus on addressing a “not to exceed” requirement
  Some USA permits require short-term (30 to 60 minute) on/off testing to evaluate turbine contribution and demonstrate compliance with “not to exceed” requirement
  Tonality assessments in USA, typically utilize one-third octave band methods rather than narrow band methods used in the EU and in IEC 61400-11
  Currently unaware of any project in the United States that had to address Amplitude Modulation (low frequency, infrasound historically concerns raised in United States)

## Slide 9: Implementation of IEC 61400-11-2
Will implementation guidance be needed for United States jurisdictions?
  One intent of IEC 61400-11-2 was to inform those countries just developing wind and wind turbine sound measurement methods
  When IEC 61400-11-2 is referenced in permit approvals, will all potential characteristics need to be tested using all methods?
  How best to ensure testing is focused on legitimate concerns?

## Slide 10: Implementation of IEC 61400-11-2
Overall challenges – where and how many locations require field testing?
  Proxy locations - locations where signal to noise ratio facilitates more robust assessment of turbine contribution.
  Experience in the United States indicates that testing at representative or proxy locations has gained regulatory acceptance
IEC 61400-11-2 will include a sound power level and modeling approach.
    Either measure sound power level at key locations or rely on vendor specifications
    Given it is often challenging to isolate turbine sound from ambient sounds, this option may provide quicker black and white answer
    While other countries utilize a similar approach (Denmark, Germany, elsewhere), USA does not yet have robust history of relying on modeling for non-transportation sound sources.

## Slide 11: Thank You