## Slide 1
IEC TC88 USTAG meeting
IEC 61400-23
Full-scale structural testing of rotor blades
Scott Hughes
9 March 2021

## Slide 2: TC88 MT23: IEC 61400-23 – Scope
Full-scale blade testing for design validation
  Property Testing
  Static Testing
  Fatigue Testing
  Documentation
  Test Planning Test Execution
  Evaluation & Reporting of Results
MT Composition
  58 Members, ~20 actively engaged
  11 Countries represented
  Convener - Søren Andersen, Denmark
  6 US experts

## Slide 3: TC88 MT23: IEC 61400-23 – Progress
Maintain scope of full-scale testing
  Excludes sub-scale components and sub-structures
  Includes less-than-full-length sub-article testing – piecewise testing of large blades
  Static, fatigue, post-fatigue sequence
Reorganization of content for more logical flow, better grouping of topics, expectations of designers and labs
Integration with IEC standards and IECRE operating documents
  Remove design validation in deference to -5 standard
  Maintain legacy information not yet prescribed in -5 or other documents
Clearer definition of areas to be tested – structurally critical areas
Guidelines for similarity testing
Developed process for handling repairs prior to and during testing
Process for evaluating influences of boundary conditions
Develop clear definition of test requirements
  Identification other tests – stiffness, lightning protection
  Modal testing - definition of requirements and test methods from 2017 ILC
  Static testing – better definition of critical load directions, option number of test directions
  Fatigue testing – graded PSFs, evaluation of design damage per material, resonant calibration methods
  Clarify requirements for uncertainty estimation
New requirements for communication of test results expectation to support test execution and QC

## Slide 4: TC88 MT23: IEC 61400-23 – Key Issues
Timeline for progress at the subgroup level
Timeline MT web and in-person meetings, expect improvements in meeting plans
Requirement for communication of test expectations may be controversial
New requirements for fatigue testing could be controversial
  Common current practice will not necessarily be grandfathered with existing safety factors
  Effort to balance end customer perception that current testing is less than fully useful with OEM perception that safety factors are too high
  Opportunities for lower SFs’ with more rigorous validation
  Concerns with equivalent damage for fiberglass, carbon, adhesive bondlines.
  Enabling paths for bi-axial fatigue testing
Clearer definition of areas to be tested could impose ‘new’ requirements
Opportunities for sub-article testing should be welcome
Lack of owner / operator engagement
Lack of standards to support some -5 model validation may disappoint

## Slide 5: TC88 MT23: IEC 61400-23 – Path Forward
IEC website lists target dates of:
  CD 2020-07 – cannot be achieved – more likely 2021-06
  IS 2020-03 – cannot be achieved – more likely 2022-06
Notional path forward
  Web meeting spring 2021 to harmonize subgroup activities
  MT23 meeting fall (US or China) 2021 to review comments on CD & produce CDV
  MT23 meeting spring 2022 to review comments on CDV & produce FDIS